## Slide 1: Chapter 4: network layer
chapter goals:
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  generalized forwarding
instantiation, implementation in the Internet

## Slide 2
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 3: Network layer
transport segment from sending to receiving host
network layer protocols in every host, router
Two key network-layer functions:
  routing: determine the path to take
  forwarding: move packets from a router’s input port to appropriate output port
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 4: Network layer: data plane, control plane
Data plane
forwarding function
local, per-router function
“which output port to forward this datagram to?”
Control plane
routing function
network-wide logic
“which path to take to reach the destination host?”
two control-plane architectures:
  per-router control plane (traditional)
  logically centralized control plane (software-defined networking (SDN))
1
2
3
0111
values in arriving
packet header

## Slide 5
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 6
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 7
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 8: Router architecture overview
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
high-level view of generic router architecture:

## Slide 9: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric
packet can be dropped due to detected error

## Slide 10: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric
packet can be dropped due to detected error

## Slide 11: Destination-based forwarding
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?
forwarding table
Notes: Where Is the Routing Table Stored?
Control Plane (CPU or Routing Engine):
  The full routing table is maintained here.
  It computes the best paths using routing protocols (e.g., OSPF, BGP).
  This is where decisions about where to forward packets are made.
Forwarding Plane (Line Cards / ASICs):
  A forwarding table (also called FIB – Forwarding Information Base) is derived from the routing table.
  This is distributed to line cards or port-level hardware for fast packet forwarding.
  It contains only the necessary information for forwarding packets (e.g., next-hop, interface).

## Slide 12: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3
Notes: first -> interface 0
second -> interface 1

## Slide 13: Longest prefix matching
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: can up ~1M routing table entries in TCAM
Notes: The Cisco Catalyst series is primarily designed for enterprise routers/switches. Their price is usually $1K – 10K, with 8-48 ports.

## Slide 14: Review
Network layer basics:
  2 key network layer functions
  Data plane vs. control plane
  Per-router control plane vs. logically centralized control plane
  Service model
Router:
  Router architecture
  Longest prefix matching
Notes: End of lecture 1.

## Slide 15: Switching fabrics
“switch” packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 16: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus
Notes: speed: 0.5 pkt / clock cyle

## Slide 17: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 6500: sufficient speed for access and enterprise routers
bus
Notes: early version of Cisco6500 (1999): up to 400 million packets per sec
speed: 1 pkt / clock cycle

## Slide 18: Switching via interconnection network
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar
Notes: speed: n pkts/clock cycle

## Slide 19: Output port functions
queueing required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
Datagram (packets) can be dropped due to buffer overflow
important for performance (delay) & fairness
Notes: Output queueing induces most of the perceived queueing delays/losses.

## Slide 20: Input/output port queueing
switching fabric is slower than input ports combined  queueing may occur at input ports (rare)
output link is slower than switching fabric  queueing may occur at output ports (common!)
  queueing causes delays and losses (due to buffer overflow)!
switching fabric
…
…
input ports
output ports
Notes: talk about the 4 components of per-hop delay: processing delay, queueing delay, transmission delay, propagation delay

## Slide 21: Scheduling policies
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Notes:   discard policy: if packet arrives to full queue: who to discard?
    tail drop: drop arriving packet
    priority: drop/remove on priority basis
    random: drop/remove randomly

## Slide 22: Scheduling policies: priority
priority scheduling: send highest priority queued packet
multiple classes, with different priorities
  class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc.
  real world example?
high priority queue
(waiting area)
low priority queue
(waiting area)
arrivals
classify
departures
link
(server)
1
3
2
4
5
5
5
2
2
1
1
3
3
4
4
arrivals
departures
packet in service
FCC to propose rules for net neutrality that ban internet providers from blocking websites | CNN Business
Notes: FCC's Current Position on Net Neutrality (2025)
The FCC has formally ended the "Restore Net Neutrality" proceeding initiated under the Biden administration.
This action is part of the FCC’s “Delete, Delete, Delete” initiative, aimed at removing outdated or burdensome regulations.
The link is a 2023 CNN article titled: FCC to reintroduce rules protecting net neutrality

## Slide 23: Scheduling policies: still more
Round Robin (RR) scheduling:
multiple classes
cyclically scan class queues, sending one complete packet from each class (if available)
1
2
3
4
5
5
5
2
3
1
1
3
2
4
4
arrivals
departures
packet in service

## Slide 24: Scheduling policies: still more
Weighted Fair Queuing (WFQ):
generalized Round Robin
each class gets weighted amount of service in each cycle
Notes: Lecture 1.

## Slide 25: Review
4 main components of a router
  Input ports, output ports, routing processor, switching fabric
3 types of switching fabrics
  Memory-based, bus-based, interconnection network-based
3 key functions at input/output ports
  line termination, link layer protocol, table lookup/queueing
4 scheduling policies
  FIFO, priority, RR, WFQ
Notes: End of lecture 2.
Input port: line termination, link layer processing (receive), forwarding table lookup; Output port: line termination, link layer processing (send), queueing and scheduling.

## Slide 26
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 27: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead
Notes: The ToS field (1 byte) has evolved over time. It is now largely replaced by the Differentiated Services (DS) field, which uses the first 6 bits for the Differentiated Services Code Point (DSCP) and the last 2 bits for Explicit Congestion Notification (ECN). DSCP enables more granular traffic classification and prioritization.
List of IP protocol numbers - Wikipedia

## Slide 28: IP fragmentation, reassembly
network links have MTU (max. transmission unit) – largest payload size (#bytes) of a link-layer frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
Notes: MTU: maximum transmission unit
MSS: maximum #bytes in the payload of a TCP segment
Example MTU:
- Ethernet: 1500 bytes
- WiFi: 2304 bytes
- Cellular (LTE/5G): up to the provider

## Slide 29: IP fragmentation, reassembly
example:
4000-byte datagram
MTU = 1500 bytes
  Both include 20 bytes of IP header

#fragments =
offset =
1480/8 = 185
20-byte header
1st 1480-byte of payload
2nd 1480-byte of payload
last 1020-byte of payload
offset =
0/8 = 0
offset =
2960/8 = 370
8 bytes
ID
=x
offset
=0
fragflag
=0
length
=4000
Notes: Q: What if MTU-20 is not a multiple of 8?
A: The IPv4 RFC says “If an internet datagram is fragmented, its data portion must be broken on 8 octet boundaries.” So the actual #bytes in the payload of an outgoing datagram will be up to 8*floor((MTU-20)/8) bytes.
For example, if MTU = 1000 bytes, then the payload can only hold 980 bytes of data (980 = 122*8 + 4). By the above rule, IP fragmentation can only pack 976 bytes of data into one fragment (length = 996).
Offset field is 13 bits long. So the maximum offset value is 2^16 bytes (64 KB), enough for maximum possible input packet length.
Flags (FragFlag) Field is 3 bits long.
These bits are:
  Reserved bit (must be zero)
  Don't Fragment (DF) flag
  More Fragments (MF) flag

## Slide 30: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 31
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 32: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
Notes: “dot decimal format”: 223.1.1.1
IPv6 address: 2001:0db8:85a3:0000:0000:8a2e:0370:7334
Each hexadecimal number represents 4 bits (value in 0-f), 8 16-bit numbers separated by “:”.

## Slide 33: Subnets
IP address:
  subnet part - high order bits shared by interfaces in the same subnet
  host part - low order bits
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
11011111 00000001 00000001 00000001
subnet
part
host
part
223.1.1.1
Notes: Subnets are important to IP because they are the “owners” of IP addresses (host “lease” from subnet when they join the subnet)

## Slide 34: Subnets
What’s a subnet ?
  device interfaces that can physically reach each other without intervening router
recipe
detach each interface from its host or router
each isolated network is called a subnet
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
Notes: Q: note that all IP addresses in the same blue bubble are similar (same prefix), is there anything in common?
A: they all belong to the same subnet.

## Slide 35: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 36: Review
IP (v4):
  Datagram format
  IP fragmentation (why? how supported by header fields?)
Subnet
  What is an IP address associated with?
  How to define a “subnet”?
Notes: End of lecture 3.

## Slide 37: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
Q: Is IP address 200.23.17.1 within this subset?
Notes: Yes!

## Slide 38: Exercise
Q1: what are all possible subnet addresses of subnet 3?
Q2: how many hosts are supported in subnet 3 using each of the above addresses?
subnet 1
subnet 2
subnet 3
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
A:
Subnet address #IP addresses
223.1.3.0/24 232-24 = 256
223.1.3.0/25 232-25 = 128
223.1.3.0/26 232-26 = 64
223.1.3.0/27 232-27 = 32

## Slide 39: IP addresses: how to get one?
Q: How does a host get IP address?
A1: hard-coded by system admin in a file
  Windows: control panel → network → configuration → tcp/ip → properties
  UNIX: /etc/rc.config
A2: DHCP (Dynamic Host Configuration Protocol): dynamically get address from as server
  “plug-and-play”
Notes: DHCP (Dynamic Host Configuration Protocol) is an application layer protocol, not a network layer control protocol. Because:
DHCP operates over UDP, using ports: Client to server: UDP port 67
Server to client: UDP port 68

## Slide 40: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg
An application-layer protocol that runs over UDP
Notes: why UDP: before DHCP, host does not even have an IP address, cannot establish connection!

## Slide 41: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 42: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src: 0.0.0.0, 68
dest: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!
Notes: 67/68: DHCP server/client port number
yiaddr: “your Internet address”
Q: why is DHCP request broadcast?
A: to notify other DHCP servers that their offers have been declined.

## Slide 43: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of local DNS sever
  subnet mask (indicating subnet versus host portion of address)

## Slide 44: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 45: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:

## Slide 46: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
→ longer prefix wins
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 47: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes
Notes: From Wikipedia: The Internet Corporation for Assigned Names and Numbers (ICANN /ˈaɪkæn/ EYE-kan) is an American multistakeholder group and nonprofit organization responsible for coordinating the maintenance and procedures of several databases related to the namespaces and numerical spaces of the Internet, ensuring the network's stable and secure operation.[2] ICANN performs the actual technical maintenance work of the Central Internet Address pools and DNS root zone registries pursuant to the Internet Assigned Numbers Authority (IANA) function contract. The contract regarding the IANA stewardship functions between ICANN and the National Telecommunications and Information Administration (NTIA) of the United States Department of Commerce ended on October 1, 2016, formally transitioning the functions to the global multistakeholder community.

## Slide 48: Review
CIDR:
  How many hosts are in a 203.12.0.0/23 subnet?
DHCP:
  How does a host obtain an IP address?
Hierarchical addressing:
  How does an organizational/ISP network obtain its block of IP addresses?
  Why is forwarding based on “longest prefix matching”?
Notes: End of lecture 4.

## Slide 49
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 50: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers
Notes: motivation: local network uses just one IP address as far as outside world is concerned:
  expand #supported devices: just one IP address for all devices
  isolation: (1) can change addresses in local network without notifying outside world, (2) can change ISP without changing addresses in local network
  security: devices inside local network not explicitly addressable by outside world
Example: my home address space: 192.168.0.0/16 (another block of private IP addresses)

## Slide 51: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 52: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 53: NAT: network address translation
16-bit port-number field:
  ~ 60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  address shortage should be solved by IPv6
  NAT traversal: what if client wants to connect to server behind NAT?
Notes: NAT is an example of “middleboxes”, i.e., a network device designed to perform functions other than routing/forwarding (other examples: firewall, IDS, load balancer, cache).

## Slide 54
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 55: IPv6: motivation
primary motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header

## Slide 56: IPv6 datagram format
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
IPv6
ver
length
data
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IPv4
+flow Label: identify datagrams in same “flow.”
-fragmentation: only performed by the source
-checksum: removed to reduce processing time at each hop
-options: allowed, but outside of header, indicated by “next hdr”
Notes: priority <-> type of service
payload length <-> length – header length
next header <-> upper layer protocol number
hop limit <-> TTL
Other changes::
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions
In IPv6, the Flow Label field is a 20-bit field in the IPv6 header used to identify packets that belong to the same flow. Routers can use this label to:
Apply consistent routing decisions
Prioritize or shape traffic
Avoid reordering packets

## Slide 57: IPv6 datagram format: more on fragmentation
-fragmentation: only performed by the source
How:
Either use IPv6 default minimum MTU of 1280 bytes
Or use Path MTU Discovery based on ICMPv6 “packet too big” message
ICMPv6 Fields:
Type 2
Code Set to 0 (zero) by the originator and ignored by the receiver.
MTU The Maximum Transmission Unit of the next-hop link.
Notes: Other changes::
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 58: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 59: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 60: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4
Notes: Q: How does B know the IPv4 address of E?
Static tunnel: manually configured
Dynamic tunnel: discovered from heartbeat messages from E
  Automatic IPv6 Connectivity Client Utility (AICCU): automatically configure the tunnel
Q: How does tunnel endpoint (E) know that the received IPv4 packet contains an IPv6 packet in the payload?
A: “protocol number” field equals 41, meaning “IPv6 Encapsulation”

## Slide 61: IPv6: adoption
By 2015, (latest stats: https://www.google.com/intl/en/ipv6/statistics.html)
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long time for deployment (why?)
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
42M IP addresses, 33 M IP links, 40K ASes
71K IPv6 addresses, 186K IPv6 links, 5K ASes
Notes: IPv6 is intended to replace IPv4.[1] In December 1998, IPv6 became a Draft Standard for the IETF,[2] who subsequently ratified it as an Internet Standard on 14 July 2017.

## Slide 62: Review
NAT:
  motivation, mechanism
IPv6 vs. IPv4
  Key differences
  Compatibility: IPv6-inside-IPv4 tunneling
Notes: End of lecture 5.

## Slide 63
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 64
Generalized Forwarding and SDN
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each router contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions
Notes: AT&T has achieved its goal of virtualizing and controlling 75% of its network functions using SDN (Software-Defined Networking) by the end of 2020. This includes a significant portion of its core network infrastructure, as part of its broader Domain 2.0 transformation initiative. [www.sdxcentral.com]
Open RAN and SDN Integration
AT&T is aggressively pursuing a multi-vendor Open RAN strategy, with partners like Ericsson, Fujitsu, and Mavenir.
By late 2026, AT&T expects 70% of its 5G traffic to traverse open hardware, managed by SDN-based platforms like Ericsson’s Intelligent Automation Platform (EIAP).

## Slide 65: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Match: values in packet header fields
  Actions: drop/forward/modify matched packet, or send matched packet to controller
  Counters: #bytes and #packets
  Priority: disambiguate overlapping patterns
Flow table in a router (computed and distributed by controller) define router’s match+action rules
Notes: Highest priority will match first.

## Slide 66: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Match: values in packet header fields
  Actions: drop/forward/modify matched packet, or send matched packet to controller
  Counters: #bytes and #packets
  Priority: disambiguate overlapping patterns
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard
Notes: Value of “priority”: the larger the value, the higher the priority.
Maximum value: priority=65535 (i.e., ‘priority’ is a 16-bit binary number)

## Slide 67: OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Match
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Notes: two more fields in OpenFlow 1.0:
VLAN Priority (link layer), IP TOS (network layer)
“4. Send to normal processing pipeline”: send to non-OpenFlow processing (lookup a traditional forwarding table)
Current stable version: 1.5 (40 fields)
Latest version: 1.6
67

## Slide 68
Destination IP-based forwarding (router):
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
Examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to output port 6
Destination MAC-based forwarding (switch):
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
22:A7:23:
11:E1:02
*
*
*
*
*
*
*
port3
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
*

## Slide 69
Examples
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward datagrams destined to port 22 (block SSH)
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward datagrams sent by host 128.119.1.1
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
10.0.0.1
*
*
3345
*
IP src ← 138.76.29.7 sport ← 5001
NAT:
translate address 10.0.0.1, 3345 to 138.76.29.7, 5001
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
138.76.29.7
*
*
5001
*
IP dst ← 10.0.0.1 dport ← 3345
Notes: IP Prot (protocol number): https://www.iana.org/assignments/protocol-numbers/protocol-numbers.xhtml

## Slide 70: OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies different kinds of devices

## Slide 71: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2
Notes: End of lecture 6.

## Slide 72
Chapter 4: done!
Question: how do forwarding tables (destination-based forwarding) or flow tables (generalized forwarding) computed?
Answer: by the control plane (next chapter)
4.1 Overview of Network layer: data plane and control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  NAT
  IPv6
4.4 Generalized Forward and SDN
  match plus action
  OpenFlow example

## Slide 73: retired slides

## Slide 74: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?
Notes: Asynchronous transfer mode (ATM)

## Slide 75: Network service model
Q: What service model for “channel” transporting datagrams from sender to receiver?
example:
guaranteed delivery
guaranteed maximum delay
guaranteed in-order delivery
guaranteed minimum bandwidth
Network
Architecture
Internet
Service
Model
best effort
Bandwidth
none
Loss
no
Order
no
Timing
no
Congestion
feedback
no (inferred
via loss)
Guarantees ?

## Slide 76: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 77: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  expand #supported devices: just one IP address for all devices
  isolation: (1) can change addresses in local network without notifying outside world, (2) can change ISP without changing addresses in local network
  security: devices inside local network not explicitly addressable by outside world

## Slide 78: Tunneling
Q: How does B know the IPv4 address of E?
  Static tunnel: manually configured
  Dynamic tunnel: discovered from heartbeat messages from E
    Automatic IPv6 Connectivity Client Utility (AICCU): automatically configure the tunnel
Network Layer: Data Plane