## Slide 1: Chapter 5: network layer control plane
chapter goals: understand principles behind network control plane
traditional routing algorithms
SDN controllers
Internet Control Message Protocol
network management
and their instantiation, implementation in the Internet:
OSPF, BGP, OpenFlow, ODL and ONOS controllers, ICMP, SNMP

## Slide 2
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 3: Network-layer functions
forwarding: move packets from router’s input to appropriate router output
data plane
control plane
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
Recall: two network-layer functions:
routing: determine route taken by packets from source to destination

## Slide 4
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 5: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or positively related to
delay
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least-cost path
Notes: link cost can represent any additive performance metric (leasing cost, delay, jitter, inverse of bandwidth, etc.)

## Slide 6: Routing algorithm classification
Q: Centralized or decentralized information?
centralized:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms

## Slide 7
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 8: A link-state routing algorithm
Dijkstra’s algorithm
network topology, link costs known to all nodes
  accomplished via “link state broadcast”
each node computes least cost paths from itself (‘source”) to all other nodes
  gives forwarding table for that node
notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor of v along the least-cost path from source to v
N': set of nodes whose least-cost paths have been found
Notes: Dijikstra: (1930-2002) a Dutch computer scientist (retired as a professor at UT Austin), who invented the algorithm at age 26.

## Slide 9: Dijkstra’s algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v), p(v) = u
6 else D(v) = ∞, p(v) =
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
for all v adjacent to w and not in N' :
if D(w) + c(w,v) < D(v)
13 D(v) = D(w) + c(w,v), p(v) = w
14 /* new cost to v is either old cost to v or known
15 shortest path cost to w plus cost from w to v */
16 until all nodes in N'

## Slide 10
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra’s algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct routing tree by tracing back the predecessors
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 11: Dijkstra’s algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 12: Dijkstra’s algorithm: example (2)
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y

## Slide 13: Dijkstra’s algorithm, discussion
algorithm complexity: n nodes
each iteration: need to check all nodes not in N’
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(n∙log(n))
  More precisely, O(n∙log(n) + |E|)
requires nonnegative link costs
Notes: Note 1: O(n*logn) assumes constant degree per node. In general, the complexity is O(n log(n) + |E|), where |E| is #links.
Note 2: Straightforward implementation using an ordered data structure to store D(v)’s (e.g., binary search tree) will cause complexity O(|E| log(n)), due to |E| distance updates each taking time O(log(n)) to update the data structure. However, using Fibonacci heap can reduce the complexity to O(|E|+n log(n)).

## Slide 14: Review
Overview
  Two key network-layer functions (routing, forwarding)
  Two control plane architectures (per-router, logically centralized)
Dijkstra’s algorithm
  a centralized, link-state routing algorithm
Notes: End of lecture 1.

## Slide 15
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 16: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 17: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 18: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 19: Distance vector algorithm
asynchronous version (in practice): each local iteration triggered by
local link cost change
DV update message from neighbor
synchronous version (in theory):
all nodes perform update-notify synchronously
wait for (change in local link cost or msg from neighbor)
update estimates
if DV to any dest has changed, notify neighbors
each node:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N

## Slide 20
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
iteration t
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
t = 0
t = 1

## Slide 21
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
iteration t
t = 0
t = 1

## Slide 22
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
iteration t
t = 0
t = 1
t = 2
DV converges in 2 iterations

## Slide 23: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
i= | t=0 | t=1 |  | 
y | 4, x |  |  | 
z | 5, y |  |  | 
source
Di(x), ni(x)
Di(x): distance from i to x
ni(x): next hop node from i to x
destination
Dy(x)=min{c(y,x)+0,c(y,z)+Dz(x)}
=min{1, 1+Dz(x)}
Dz(x)=min{c(z,x)+0,c(z,y)+Dy(x)}
=min{50, 1+Dy(x)}
1, x
-
t=2
-
2, y

## Slide 24: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
i= | t=0 | t=1 | t=2 | t=3
y | 4, x | 1, x | - | 1, x
z | 5, y | - | 2, y | 2, y
source
Di(x), ni(x)
Di(x): distance from i to x
ni(x): next hop node from i to x
converge!
destination

## Slide 25: Review
Distance Vector (DV) algorithm:
  Bellman-Ford equation
  DV table and its iterative calculation
  DV under link cost change
    Count-to-infinity problem, poisoned reverse
Notes: End of lecture 2.

## Slide 26: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slowly - “count to infinity” problem!
How many iterations to converge?
x
z
1
4
50
y
60
destination
i= | t=0 |  |  |  |  |  |  |  |  | 
y | 4, x |  |  |  |  |  |  |  |  | 
z | 5, y |  |  |  |  |  |  |  |  | 
Di(x): distance from i to x
ni(x): next hop node from i to x
Dy(x)=min{c(y,x)+0,c(y,z)+Dz(x)}
=min{60, 1+Dz(x)}
Dz(x)=min{c(z,x)+0,c(z,y)+Dy(x)}
=min{50, 1+Dy(x)}
t=1
6, z
-
t=2
-
7, y
t=3
8, z
-
t=44
48, z
49, y
...
...
...
t=45
50, z
-
t=46
-
50, x
t=47
51, z
-

## Slide 27: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slowly - “count to infinity” problem!
How many iterations to converge?
x
z
1
4
50
y
60
destination
i= | t=0 | t=1 | t=2 | t=3 | ... | t=44 | t=45 | t=46 | t=47 | t=48
y | 4, x | 6, z | - | 8, z | ... | 48, z | 50, z | - | 51, z | 51, z
z | 5, y | - | 7, y | - | ... | 49, y | - | 50, x | - | 50, x
Di(x): distance from i to x
ni(x): next hop node from i to x
converge!
routing in cycle!
Notes: Condition for breaking the cycle: node z realizes that directly routing to x is better than routing to x through y

## Slide 28: Distance vector: link cost changes
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
How many iterations to converge with poisoned reverse?
destination
i= | t=0 |  |  |  | 
y | 4, x |  |  |  | 
z | 5, y |  |  |  | 
Dy(x)=min{c(y,x)+0,c(y,z)+Dz(x)}
=min{60, 1+Dz(x)}
Dz(x)=min{c(z,x)+0,c(z,y)+Dy(x)}
=min{50, 1+Dy(x)}
t=1
60, x
-
t=2
-
50, x
t=3
51, z
-

## Slide 29: Distance vector: link cost changes
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
How many iterations to converge with poisoned reverse?
destination
i= | t=0 | t=1 | t=2 | t=3 | t=4
y | 4, x | 60, x | - | 51, z | 51, z
z | 5, y | - | 50, x | - | 50, x
converge!
Q: will poisoned reverse eliminate the “count to infinity” problem?
Notes: No. Example: see HW5 Problem 2 (c).

## Slide 30: Review
Distance vector algorithm
  #iterations till convergence
  “count to infinity” and poisoned reverse
Notes: Lecture 3.

## Slide 31
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 32: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
all routers must run same inter-domain protocol
intra-AS routing
all routers in an AS must run same intra-domain protocol
routers in different ASes can run different intra-domain protocols
our routing study thus far assumes -
all routers are identical
network is “flat”
not true in practice
Notes: e.g., OSPF (Open Shortest Path First) is basically Dijkstra’s algorithm
IGP: interior gateway protocols
BGP: boarder gateway protocol

## Slide 33: Configuration of Forwarding Table
suppose router 1a in AS1 receives a datagram destined to host h:
if h is in AS1:
learn next hop on the shortest path to h (intra-AS routing)
if h is outside AS1:
learn which gateway router to forward to (inter-AS routing)
learn next hop to go to that gateway (intra-AS routing)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
Notes: talk about the tasks to route to a remote destination from the perspective of router 1a

## Slide 34: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): provides each AS a means to:
  eBGP: obtain subnet X reachability information from neighboring ASes
  iBGP: propagate reachability information to all internal routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X
eBGP connectivity
iBGP connectivity
Notes: IGP: interior gateway protocol (a family of intra-AS routing protocols)
eBGP: external BGP
iBGP: internal BGP
BGP relies on each subnet to advertise its existence to rest of Internet: “I am here”
(e/i)BGP connection: two BGP routers exchange BGP messages over semi-permanent TCP connection

## Slide 35: Path attributes and BGP routes
BGP advertisement includes: destination prefix & BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: IP address of the router interface that starts the AS-PATH
See full list of BGP attributes at: http://www.networkers-online.com/blog/2012/05/bgp-attributes/
Notes: Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other neighboring ASes
RFC 4271 defined Next-Hop attribute as follows:
The NEXT_HOP is a well-known mandatory attribute that defines the IP address of the router that SHOULD be used as the next hop to the destinations listed in the UPDATE message.

## Slide 36: BGP route advertisement
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
prefix: X
AS-PATH: AS3
NEXT-HOP: IP1
prefix: X
AS-PATH: AS2,AS3
NEXT-HOP: IP2
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
IP1
IP2

## Slide 37: BGP + IGP
1a, 1b, 1d learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: by intra-domain routing: to get to 1c (IP1), forward to outgoing interface 1
AS3,X
AS2,AS3,X
Q: how does router set forwarding table entry to remote prefix?
1
2
1
2
dest
interface
IP1
…
X
1
…
1
IP1
Notes: IGP: interior gateway protocol (i.e., intra-AS routing protocol)
1d does not know how to forward packet to interface at 2a, solutions:
advertise 1c-2a subnet within AS1 (not recommended)
use “Next-Hop Self” option (recommended), which rewrites NEXT-HOP attribute to an IP address at 1c (for the interface used by a given iBGP connection).

## Slide 38: receiving multiple BGP advertisements
1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
A gateway router may learn multiple paths to a destination:
AS3,X
1c learns path AS3,X from 3a
1c will perform BGP route selection to choose a path and advertise this path within AS1

## Slide 39: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP: hot potato routing
  additional criteria (e.g., advertisement received first)
An example of complete criteria: https://www.cisco.com/c/en/us/support/docs/ip/border-gateway-protocol-bgp/13753-25.html
Notes: Local preference: pick the route(s) with the highest local preference value
Examples of additional criteria: oldest route (receives advertisement first), route heard from a router with the lowest ID, etc.

## Slide 40: Review
BGP:
  iBGP, eBGP
  BGP “route”: prefix + attribute
  Policy-based routing: BGP route advertisement, BGP route selection
Notes: End of lecture 4.

## Slide 41
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 42
data
plane
control
plane
SDN: Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 43: Traffic engineering is difficult for traditional routing
Q: what if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xyz?
A: need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 44: Traffic engineering: difficult
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 45: Traffic engineering: difficult
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route blue and red traffic differently?
A: can’t do it (with destination based forwarding)
Networking 401
Notes: Note: implicit assumption here: destination based forwarding

## Slide 46
Software defined networking (SDN)
Why SDN? (instead of the traditional per-router control plane architecture)
easier network management: avoid router misconfigurations
greater flexibility: generalized forwarding allows “programming” routers
open (non-proprietary) implementation of control plane

## Slide 47
Components of SDN
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: switches generalized“ flow-based” forwarding (e.g., OpenFlow)
2. controller control plane functions external to data-plane switches
…
3. control applications programmable applications using controller APIs
routing
access control
load
balance

## Slide 48
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized forwarding (Section 4.4)
switch flow table computed, installed by controller
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
Notes: Example OpenFlow messages: “packet in” (report a new flow to controller) -> “flow mod” (install a new rule) -> “flow removed” (rule removed from flow table)
Latest version: OpenFlow 1.6 (2016), latest stable version (open to public): OpenFlow 1.5.1

## Slide 49
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
Note: (often) implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
Notes: Common SDN controllers: OpenDayLight (Java), Floodlight (Java), Ryu (Python), ONOS (Open Network Operating System; Java), NOX (C++), POX (Python)

## Slide 50
SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using APIs provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 51
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
S1, experiencing link failure using OpenFlow “port status” message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when- ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4

## Slide 52
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
Routing app interacts with flow-table-computation component in SDN controller, which computes new flow rules needed
5
Controller uses OpenFlow “flow mod” messages to install new rules in switches that need updating
6

## Slide 53
Review
SDN
  Why using SDN (vs. traditional routing)?
  What are the three components of an SDN?
  What are the three main functions of an SDN controller?
Notes: End of lecture 5.

## Slide 54
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 55: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
ICMP message: type, code, and header plus first 8 bytes payload of the IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header
ICMP runs over IP!
Internet Control Message Protocol
Notes: ICMP’s Protocol Number (in IP header): 1
Two examples of “messages encapsulated into IP datagrams”: OSPF (link state) message, ICMP message
TTL: “TTL” field in IPv4, “hop limit” field in IPv6, decremented by 1 at each router, triggers “TTL expired” error message when reaching 0
ICMP error messages contain a data section that includes a copy of the entire IPv4 header, plus at least the first eight bytes of data from the IPv4 packet that caused the error message. The length of ICMP error messages should not exceed 576 bytes. (If a higher level protocol uses port numbers, they are assumed to be in the first eight bytes of the original datagram's data.)

## Slide 56: Traceroute and ICMP
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message include name of router & IP address
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
Notes: Traceroute can use UDP, ICMP Echo Request or TCP SYN packets (by default, it uses UDP).

## Slide 57
Q1: Does traceroute have to use UDP packets?
A1: No. Can also use others (e.g., TCP SYN packets, ICMP Echo Request).
Q2: Does traceroute always return correct information?
A2: No. Multipath routing can cause errors.
Q3: Does traceroute monitor every link?
A3: No. Need collaboration of multiple sources (beacons).
  Beason Placement Problem: Select a minimum set of beacons such that their routing trees cover all the links.
Traceroute beyond ICMP
Load balancing
Beacon v
Links in routing tree of v
NP-hard (set cover problem)!
Notes: If time allows, do a local->remote and remote->local traceroute experiment (by picking a server in traceroute.org).
Example Internet measurement project from CAIDA: Archipelago Monitor Locations - CAIDA

## Slide 58
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 59: Infrastructure for network management
managed device
managed device
managed device
managed device
definitions:
managed devices contain managed objects whose data is gathered into a Management Information Base (MIB)
managing
entity
data
managing entity
agent
data
agent
data
network
management
protocol
managed device
agent
data
agent
data
agent
data
Notes: “network management”: monitor & control network devices (hosts, routers, switches) to achieve desired QoS.
network management as an application is a client-server architecture application; client -> agent, server -> managing entity
kind of a “reverse HTTP”: manager requests MIB objects from agents

## Slide 60: Simple Network Management Protocol (SNMP)
Two ways to convey MIB info, commands:
agent
data
managed device
managing
entity
agent
data
managed device
managing
entity
trap msg
request
request/response mode
trap mode
response

## Slide 61: SNMP protocol: message types
GetRequest
GetNextRequest
GetBulkRequest
manager-to-agent: “get me data”
(data instance, next data in list, block of data)
Message type
Function
InformRequest
manager-to-manager: here’s MIB value
SetRequest
manager-to-agent: set MIB value
Response
Agent-to-manager: value, response to
Request
Trap
Agent-to-manager: inform manager
of exceptional event
request/ response mode
trap mode
bootstrap manager
initialize agent
SNMP runs over UDP
Notes: SNMP message is also called PDU (“protocol data unit”)

## Slide 62: Chapter 5: summary
we’ve learned a lot!
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF, BGP
SDN controllers
  implementation in practice: ODL, ONOS
Internet Control Message Protocol
network management
next stop: link layer!
Notes: Lecture 4.

## Slide 63: retired slides

## Slide 64
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 65
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 66: Routing protocols
Routing protocol goal: determine “good” paths (a.k.a. routes), from sending hosts to receiving host, through network of routers
path: sequence of routers (or links) packets will traverse
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!

## Slide 67: Dijkstra’s algorithm, discussion
algorithm complexity: n nodes
each iteration: need to check all nodes not in N’
n(n-1)/2 comparisons: O(n2)
more efficient implementations possible: O(n∙logn)
  More precisely, O(n∙logn + |E|)
requires nonnegative link costs
oscillations possible:
e.g., suppose link cost equals amount of carried traffic:
A
D
C
B
1
1+ε
ε
0
ε
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing…
2+ε
0
0
0
1+ε
1
A
D
C
B
given these costs,
find new routing…
0
2+ε
1+ε
1
0
0
A
D
C
B
given these costs,
find new routing…
2+ε
0
0
0
1+ε
1
Notes: Note: O(n*logn) assumes constant degree per node. In general, the complexity is O(n log(n) + |E|), where |E| is #links.

## Slide 68: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 69: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
speed of convergence
LS: converge in O(n) iterations (O(n2) time)
DV: convergence time varies
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS: node can advertise incorrect link cost
DV: node can advertise incorrect path cost
Notes: n: #nodes
E: #links

## Slide 70: Making routing scalable
scale: with billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice

## Slide 71: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing
  intra-AS routing determine entries for internal destinations
  inter-AS & intra-AS determine entries for external destinations

## Slide 72: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First (IS-IS protocol essentially same as OSPF)
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary for decades, until 2016)

## Slide 73: OSPF (Open Shortest Path First)
“open”: publicly available
uses link-state algorithm
  topology map at each node
  route computation using Dijkstra’s algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  When: when a link’s state changes, or every 30 minutes
  How: carried in OSPF messages directly over IP (rather than TCP or UDP)
  Which links: for each attached link

## Slide 74: OSPF “advanced” features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 75: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 76: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’es.
Notes: Lecture 2.

## Slide 77: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols
X

## Slide 78: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
(e/i)BGP connection: two BGP routers exchange BGP messages over semi-permanent TCP connection:
  used to advertise routes to different destination prefixes
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X
eBGP connectivity
iBGP connectivity

## Slide 79: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263

## Slide 80
Software defined networking (SDN)
Internet network layer: historically has been implemented via distributed, per-router approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane

## Slide 81
Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of routing flows
generalized forwarding (recall OpenFlow API) allows “programming” routers
open (non-proprietary) implementation of control plane

## Slide 82
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API
Notes: Example of open-source controller: OpenDaylight, ONOS, Ryu, etc.

## Slide 83
SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: “baked in” from day one?
flow migration/reconfiguration
  transient congestion, policy violation, synchronization
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling
Notes: Lecture 3.

## Slide 84: What is network management?
autonomous systems (aka “network”): 1000s of interacting hardware/software components
"Network management includes the deployment, integration
and coordination of the hardware, software, and human
elements to monitor, test, poll, configure, analyze, evaluate,
and control the network and element resources to meet the
real-time, operational performance, and Quality of Service
requirements at a reasonable cost."

## Slide 85: SNMP protocol: message formats
….
PDU
type
(0-3)
Request
ID
Error
Status
(0-5)
Error
Index
Name
Value
Name
Value
….
PDU
type
4
Enterprise
Agent
Addr
Trap
Type
(0-7)
Specific
code
Time
stamp
Name
Value
Get/set header
Variables to get/set
Trap header
Trap info
SNMP PDU (protocol data unit)
“UDP is the preferred transport mapping”. --- RFC 3417
Notes: End of lecture 6.