## Slide 1: Chapter 6: Link layer and LANs
our goals:
understand principles behind link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks: Ethernet, VLANs
instantiation, implementation of various link layer technologies

## Slide 2: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 3: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels between adjacent nodes: links
data-link layer’s responsibility is to
transfer datagram from one node to physically adjacent node
controller
CPU
controller
CPU
sending host
receiving host
datagram
datagram
datagram
frame
NIC
NIC
link layer’s communicating entity: adaptor
Notes: from one (layer-3) node to the next-hop (layer-3) node (i.e., from source host to first-hop router, between adjacent routers, or from last-hop router to destination host)

## Slide 4: Link layer services
link access:
  medium access control (MAC) if shared medium
error detection/correction:
  detection: receiver detects presence of errors
  correction: receiver localizes errors & fixes them
reliable delivery between adjacent nodes (optional):
  seldomly used on low bit-error link (fiber, some twisted pair)
  commonly used on high bit-error link (wireless)
    Q: why both link-level and end-end reliability?
Notes: A: 1. heterogeneous links on e2e path, need mechanism to guarantee e2e reliability as long as at least one link is not reliable;
2. low bit-error link: best to enforce reliability at endpoints (layer-4); high bit-error link: best to enforce reliability at the link (layer 2)

## Slide 5: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 6: Error detection
EDC= Error Detection and Correction bits
D = Data protected by error checking
f(.) = EDC code
otherwise
f(D)
f(D’) = EDC’?
drop

## Slide 7: Parity checking
1-D parity check:
detect single bit errors
2-D parity check:
detect and correct single bit errors
0
0
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
odd parity check: total #1’s is odd
even party check: total #1’s is even
Notes: 2-dimensional parity check can detect (not correct) any 2 bit errors. Why?
odd parity check: total #1’s is odd
even party check: total #1’s is even

## Slide 8: Internet checksum (review)
sender:
treat segment contents as sequence of 16-bit integers X1, X2,...
checksum: X1+X2+... (with wraparound), then take the complement sum
sender puts checksum value into UDP/TCP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected
goal: detect single bit errors & most multiple bit errors
some multiple bit errors are undetectable

## Slide 9: Cyclic redundancy check (CRC)
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D’,R’> by G. If non-zero remainder: error detected!
  can detect all odd number errors & burst errors of < r+1 bits
  burst error ≥ r+1 bits can be detected with prob. 1-0.5r
widely used in practice (Ethernet, 802.11 WiFi, ATM)
Notes: Ethernet: CRC-32 (G is 33-bit long)
USB: CRC-16-IBM

## Slide 10: CRC example
want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R to satisfy:
R = remainder[ ]
D.2r
G
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
no borrow!
Notes: D*2^r: dividend
G: divisor
result: quotient
leftover: remainder

## Slide 11: Review
Link layer overview:
  Link layer services
  What are the communication endpoints at link layer?
Error detection codes:
  Parity check (1D, 2D)
  Checksum
  CRC
Notes: End of lecture 1.

## Slide 12: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 13: Multiple access links, protocols
two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)
coordinated by MAC protocols
Notes: In link layer terminology, “access a link” = “transmit on a link”
wireless links are often shared (e.g., WiFi link, satellite link); but wired links can also be shared (e.g., old-fashioned Ethernet link)

## Slide 14: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns
Notes: Let’s look at what have been developed so far.
These three classes basically represent three approaches to multi-access control.

## Slide 15: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each node gets a fixed slot (length = packet transmission time) in each round
unused slots go idle
example: 6-node LAN
1
3
4
1
3
4
6-slot
round
6-slot
round
Notes: partition time into slots (each of L/R seconds for packet length L bits and link capacity R bps) -> group slots into rounds (n nodes, then every n slots is a round)
-> assign slots in each round to the nodes.
If a node (e.g., node 2) has no data in a round, its slot will remain empty (i.e., the channel will be idle during that slot).

## Slide 16: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each node assigned fixed frequency band
unused frequency bands go idle
example: 6-node LAN
frequency bands
time
FDM cable
Notes: Good things about channel partitioning protocols: simple, deterministic, collision-free
Drawbacks: low efficiency

## Slide 17: Random access protocols
node sends packets probabilistically
  fully decentralized (no a priori coordination among nodes)
two or more transmitting nodes ➜ “collision”
random access MAC protocol specifies:
  when to transmit
  how to recover from collisions
examples:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA
Notes: Adapting to demands by only letting nodes that have data to send probabilistically compete for channel access.

## Slide 18: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success
1970: ALOHAnet satellite network in Hawaii (“Additive Links On-line Hawaii Area”)
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 19: Slotted ALOHA
efficiency: long-term fraction of successful slots (assuming nodes all with infinitely many frames to send)
Suppose: N nodes, each transmits with prob. p
Q1: Prob. that a given node has success = p(1-p)N-1
Q2: Prob. that any node has a success (efficiency) = Np(1-p)N-1
Q3: The p* that maximizes efficiency = 1/N
Q4: Taking limit of the max efficiency as N goes to infinity = 1/e
at best: Channel used for useful transmissions 1/e = 37% of time!
!

## Slide 20: Pure (unslotted) ALOHA
unslotted ALOHA: simpler, no synchronization
collision probability:
  frame sent at [t-1,t] collides with frames sent at t-1 and t
node i’s frame
t-1
t
t+1
node j’s
time system
will collide with node i
will collide with node i
Q1: P(success by node i) = P(node i transmits).P(no other transmits in [t-1,t+1]
= p . (1-p)2(N-1)
Q2: P(success by any node) = N . p . (1-p)2(N-1)
Q3: optimum p* = 1/(2N-1)
Q4: limit when N → ∞: 1/(2e) = 0.18
even worse!
efficiency
Notes: Lecture 1.

## Slide 21: Review
Multiple access protocols
  What are the 3 broad classes of multiple access protocols?
  What do they control?
  Channel partitioning protocols: TDMA, FDMA
  Random access protocols: pure/slotted ALOHA
Notes: End of lecture 2.

## Slide 22: CSMA (carrier sense multiple access)
CSMA: “listen before transmit”
if channel sensed idle: transmit entire frame
if channel sensed busy, defer transmission
Q: is CSMA collision-free?
Notes: ALOHA: don’t look, don’t listen, just randomly decide at each time whether you will talk or not
CSMA: listen before you talk

## Slide 23: CSMA collisions
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in determining collision probability
A B C D
Notes: The fact that you don’t hear anyone talking does not mean no one is talking.
Therefore, a CSMA protocol should still have mechanism to recover from collision.

## Slide 24: CSMA/CD (collision detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  If collisions detected, abort transmission
collision detection:
  measure signal strengths, compare transmitted and received signals
Notes: One way to recover from collision under CSMA is collision detection.
The idea is, after you sense an idle channel and start transmitting, keep listening on the channel in case there is a remote transmission that is still propagating.
Once you detect a collision, abort current transmission (as it won’t be successful anyway) and try again later.

## Slide 25: Ethernet CSMA/CD algorithm
NIC receives datagram from network layer, creates frame.
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame!
4. If NIC detects another transmission while transmitting, aborts and sends jam signal.
5. After aborting, NIC enters binary (exponential) backoff:
  After mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K· (512 bit time), returns to Step 2.
Notes: Ethernet’s MAC protocol uses CSMA/CD combined with another idea: exponential backoff. Here is how it works...
The efficiency of CSMA/CD is determined by two parameters: t_prop and t_trans
It shows that in theory, we could use CSMA/CD to increase efficiency to 1 (as t_prop goes to 0 or t_trans goes to infinity).

## Slide 26: “Taking turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 27: “Taking turns” MAC protocols
polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
  Example: Bluetooth protocol
master
slaves
poll
data

## Slide 28: “Taking turns” MAC protocols
token passing:
control token passed from one node to next sequentially.
token frame
concerns:
  token overhead
  latency
  single point of failure (token)
  Example: FDDI (fiber distributed data interface), token ring protocol
T
data
(nothing
to send)
T
Notes: FDDI: fiber distributed data interface
If you think of polling protocol as a “client-server” based taking turns protocol, then token passing protocol is the P2P counterpart.

## Slide 29: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring

## Slide 30: Review
Multiple access protocols
  What are the 3 broad classes of multiple access protocols?
  What do they control?
  Channel partitioning protocols: TDMA, FDMA
  Random access protocols: pure/slotted ALOHA, CSMA, CSMA/CD
  Taking-turns protocols: polling, token passing
Notes: End of lecture 3.

## Slide 31: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 32: MAC addresses
IP address: 32-bit (v4) or 128-bit (v6)
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or physical) address:
  function: used “locally” to get frame from one interface to another interface within the same subnet
  48 bit MAC address (for most LANs) burned in NIC ROM
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
Notes: E.g., 1A: 00011010

## Slide 33: MAC addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
IP hierarchical address ➜ not portable
  address depends on subnet to which node is attached

## Slide 34: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
A
C
B
D
Notes: Corresponding to DNS service for IP address.
Human analogy: translating postal address into SSN

## Slide 35: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with B's MAC address
  frame sent to A’s MAC address (unicast)
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
A
C
B
D
Notes: Compared to: Manually entering entries in DNS database.
Each adaptor compares the received frame’s destination MAC address with its own MAC address, and only passes the contained datagram to its network layer if the MAC addresses match.

## Slide 36: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address (how?)
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
Notes: A1: from DNS server
A2: from DHCP server
A3: from ARP

## Slide 37: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 38: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 39: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 40: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
Notes: Lecture 2.

## Slide 41: Review
Link layer addressing:
  What is MAC address associated with? How is it different from IP address?
  ARP (address resolution protocol): What is it used for? How does it work?
Notes: End of lecture 4.

## Slide 42: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 43: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
star: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star

## Slide 44: Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
“self-synchronized”: preamble used to synchronize receiver & sender clocks
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 45: Ethernet frame structure (more)
addresses: source & destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP query), it passes data to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
  EtherType values
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type
Notes: Type 0x0806 (“0x” means hexadecimal, i.e., type field is 2-byte long) means the Ethernet frame contains an ARP in the payload.
Ethernet uses a 32-bit CRC.

## Slide 46: Switch table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (destination MAC address, output interface, time stamp)
  looks like a routing table, but configured differently
Notes: A can talk to A’ while B talks to B’ and C talks to C’ simultaneously, without collision, as the switch will selectively forward each frame towards the intended destination.

## Slide 47: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface Time
Switch table
(initially empty)
A
1
9:32

## Slide 48: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 49: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface Time
switch table
(initially empty)
A
1
9:32
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
A’
4
9:39
selectively send
on just one link

## Slide 50: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both look up tables:
routers: compute tables using routing algorithms
switches: learn forwarding actions using self-learning
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 51: Review
Ethernet:
  What is the benefit of using switch instead of bus/hub?
  How is switch table configured?
  What are the similarities and differences between switch and router?
Notes: End of lecture 5.

## Slide 52: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 53: VLANs: motivation
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering

## Slide 54: VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 55: Benefits of VLAN
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers
Notes: consequence of partitioning switch ports into multiple groups

## Slide 56: VLANS spanning multiple switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla Ethernet frames (must carry VLAN ID info)
  802.1Q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1
Notes: Ethernet is standardized in 802.3
“trunk port” is a special type of port supported by VLAN-capable switches to connect different physical switches.

## Slide 57
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (3 bit priority field like IP TOS ,
1 bit Canonical Format Indicator, 12 bit VLAN ID field)
Recomputed
CRC
802.1Q VLAN frame format
Ethernet frame
(802.3)
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type
Notes: Lecture 3.
Canonical Format Indicator: always 0 for Ethernet frame (CFI = 1 is used for Token Ring LAN frame)

## Slide 58: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 59: MultiProtocol Label Switching (MPLS)
initial goal: high-speed IP forwarding using fixed length label (instead of IP prefix)
  fast lookup using fixed length identifier (rather than longest prefix matching)
  borrowing ideas from Virtual Circuit (VC) approach
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
5
1

## Slide 60: MPLS-capable routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
flexibility: MPLS forwarding decisions can differ from those of IP
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths (useful for VoIP)
2

## Slide 61: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
IP routing: path to destination determined by destination address alone
R4

## Slide 62: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path to destination can be based on source and destination address
  fast reroute: precompute backup routes in case of link failure
entry router (R4) can use different MPLS routes to A based on source address

## Slide 63: MPLS signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing,
  e.g., link bandwidth, amount of “reserved” link bandwidth
D
R4
R5
A
R6
entry MPLS router uses RSVP-TE (resource reservation protocol – traffic engineering) signaling protocol to set up MPLS forwarding at downstream routers
modified
link state
flooding
RSVP-TE

## Slide 64
Both generalize IP-based forwarding
Different approaches:
  MPLS: extend packet header, simplify lookup, incompatible with non-MPLS-capable routers
  SDN: same packet header, generalize lookup, compatible with non-SDN-enabled switches
MPLS versus SDN

## Slide 65: Chapter 6: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
link-layer technologies in practice
  Ethernet
  switched LANS, VLANs
  virtualized networks as a link layer: MPLS
synthesis: a day in the life of a web request
Notes: End of lecture 6.

## Slide 66: SKIPPED SLIDES

## Slide 67: Link layer services (more)
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 68: Where is the link layer implemented?
in every host, router, switch
link layer implemented in “adaptor” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network interface card
application
transport
network
link
link
physical

## Slide 69: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
Notes: MAC for point-to-point link is pretty trivial, but MAC for broadcast link is tricky. Accordingly, a family of protocols have been developed to control how to access the shared link, known as “multiple access protocols”.

## Slide 70: An ideal multiple access protocol
given: broadcast channel of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple
Notes: If you were tasked to develop a multi-access protocol, what would you like to achieve?

## Slide 71: CSMA/CD efficiency
tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA, and simple, cheap, decentralized!
Derivation skipped
Notes: not required to memorize this formula
The efficiency of CSMA/CD is determined by two parameters: t_prop and t_trans
It shows that in theory, we could use CSMA/CD to increase efficiency to 1 (as t_prop goes to 0 or t_trans goes to infinity).

## Slide 72: MAC addresses and ARP
each adapter on LAN has unique MAC address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 73: Ethernet
“dominant” wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simple, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch
Notes: Robert Melancton Metcalfe (born April 7, 1946[2]) is an electrical engineer from the United States who co-invented Ethernet, founded 3Com and formulated Metcalfe's Law. As of January 2006, he is a general partner of Polaris Venture Partners. Starting in January 2011, he holds the position of Professor of Electrical Engineering and Director of Innovation at The University of Texas at Austin

## Slide 74: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff
Notes: So Ethernet is an example of a link layer protocol that does not provide reliable delivery guarantee. (kind of like UDP, but for link layer)

## Slide 75: Ethernet switch
link-layer packet switch
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links; when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 76: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Notes: this is about “selective forwarding” functionality of Ethernet switch

## Slide 77: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to I - how does S1 know to forward frame destined to I via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 78: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 79: Data center networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center

## Slide 80
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)
Internet

## Slide 81
Data center networks
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy
Notes: Source: A salable, commodity datacenter network architecture, SIGCOMM 2008.

## Slide 82: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
64 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 83: Synthesis: a day in the life of a web request
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 84: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 85: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 86: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 87: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 88: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 89: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established (for client!)
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 90: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
Notes: Lecture 4.