## Slide 1: Chapter 3: Transport Layer
our goals:
understand principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about Internet transport layer protocols:
  UDP: connectionless transport
  TCP: connection-oriented reliable transport
  TCP congestion control

## Slide 2: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 3: Transport services and protocols
provide logical end-to-end communication between app processes on different hosts
transport protocols run in hosts
  sender side: breaks app messages into segments, passes to network layer
  rcver side: reassembles segments into messages, passes to app layer
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 4: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
mix data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
Notes: Analogy: host -> dorm building, process -> occupant, socket -> mail slit on dorm door, transport layer -> intra-dorm mail service

## Slide 5: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 6: Connectionless demultiplexing
when host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
UDP socket is uniquely identified by a pair:
  (destination) IP address
  (destination) port #
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at dest

## Slide 7: Connectionless demux: example
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?
IP address: A
IP address: C
IP address: B
Notes: code is for socket programming in Java

## Slide 8: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values to direct segment to appropriate socket
server host uses different TCP sockets for different clients:
  e.g., web server creates a new socket for each connecting client
  non-persistent HTTP will have a different socket for each request

## Slide 9: Connection-oriented demux: example
transport
application
physical
link
network
P1
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
IP address: A
IP address: C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
IP address: B
port# 9157
port# 5775 port# 9157
Notes: In practice, the web server is usually implemented by a single process, using multiple threads to send/receive through the multiple TCP sockets

## Slide 10: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 11: UDP: User Datagram Protocol [RFC 768]
“best effort” service: UDP segments may be
  lost
  delivered out-of-order
connectionless
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP (more in chapter 5)
  application-layer reliable transfer protocol: e.g., Google’s QUIC protocol
no connection establishment delay
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away as fast as desired
why is there a UDP?

## Slide 12: UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
why is there a checksum?

## Slide 13: UDP checksum
sender:
treat segment contents, including header fields, as sequence of 16-bit integers
checksum: sum of the 16-bit integers with wraparound, then take complement
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But there may be errors nonetheless!
Goal: detect “errors” (e.g., flipped bits) in transmitted segment
Notes: What is included in TCP/UDP checksum calculation?
1. Pseudo Header (not transmitted, but used in checksum calculation)
Source IP address
Destination IP address
Protocol number (6 for TCP, 17 for UDP)
TCP/UDP length
2. TCP or UDP Header
Includes fields like source port, destination port, sequence number (TCP), length (UDP), etc.
3. Payload (Data)

## Slide 14: Internet checksum: example
example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit
Q: What if the #bits is not an integer multiple of 16?
A: pad 0 at the end

## Slide 15: Internet checksum: exercise
Data:
  00111010 00111111, 11100001 11100111, 00111010 00111111, 11100001 11100111
Checksum:
  11000111 10110001
00111010 00111111
+11100001 11100111
1 00011100 00100110
+1
00011100 00100111
+00111010 00111111
01010110 01100110
+11100001 11100111
1 00111000 01001101
+1
¬00111000 01001110
11000111 10110001

## Slide 16: Review
Multiplexing/demultiplexing
  what information is used for TCP/UDP socket
UDP
  advantages of UDP
  applications using UDP
  checksum
Notes: End of lecture 1

## Slide 17: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 18: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
important in application, transport, link layers
  top-10 list of important networking topics!

## Slide 19: Reliable data transfer: getting started
we’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 20: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
  no reordering of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 21: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender
How do humans recover from “errors”
during conversation?
Notes: focusing on recovering from detectable errors (errors undetected by checksum are not “errors” to rdt protocols)

## Slide 22: rdt2.0: channel with bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  feedback: control msgs (ACK,NAK) from receiver to sender

## Slide 23: rdt2.0: FSM specification
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 24: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 25: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L
stop and wait
sender sends one packet,
then waits for receiver
response

## Slide 26: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt

## Slide 27: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L
Notes: 3 differences: 1. add sequence number to pkt header, 2. treat corrupted ACK as NAK, 3. after done with pkt i, wait for pkt (i+1) mod 2

## Slide 28: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
Notes: Q: What is receiver always sends NAK when not receiving the packet it wants?

## Slide 29: rdt2.1: discussion
sender:
must check if received ACK/NAK corrupted
twice as many states
  state indicates whether the inflight pkt has seq# 0 or 1
two seq. #’s (0,1) will suffice. (Why?)
receiver:
must check if received packet is duplicate
  state indicates whether the expected seq# is 0 or 1

## Slide 30: Review
rdt1.0: no error
rdt2.0: error at receiver
  ACK/NAK
rdt2.1: error at sender & receiver
  ACK/NAK, sequence number (0/1)
Notes: End of lecture 2

## Slide 31: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last correctly received pkt
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 32: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK,1, checksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 33: rdt3.0: channels with errors and loss
new assumption: underlying channel can also lose packets (data, ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help … but not enough
approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but seq. #’s already handles this

## Slide 34: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0 from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L
Q: rdt3.0 receiver?
Notes: A: Same as rdt2.2 receiver (already handles lost packets).
Note: in case of corrupted/duplicate ACK, if the sender resends sndpkt immediately, instead of waiting for timeout, then it could trigger a sequence of duplicate pkts/ACKs if the duplicate ACK was triggered by a duplicate pkt (due to premature timeout).

## Slide 35: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 36: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
ack1
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0

## Slide 37: Extension: multi-to-one rdt
Q: How to ensure C receives alternatingly from A and B in the presence of errors/losses?
C
A
B
A: Sender A or B is the same as the sender in rdt3.0!

## Slide 38: Extension: multi-to-one rdt
Receiver C
Wait for 1 from B
Wait for 0 from B
Wait for 0 from A
Wait for 1 from A
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
(9)
(10)
(11)
(12)

## Slide 39: Extension: multi-to-one rdt
Receiver C
rdt_rcv(rcvpkt)&&from_B(rcvpkt)
sndpkt=make_pkt(ACK, 1, checksum)
udt_send(B,sndpkt)
rdt_rcv(rcvpkt) && from_A(rcvpkt)
&& (corrupt(rcvpkt) || has_seq1(rcvpkt))
sndpkt=make_pkt(ACK, 1, checksum)
udt_send(A,sndpkt)
rdt_rcv(rcvpkt)&&from_A(rcvpkt)
sndpkt=make_pkt(ACK, 0, checksum)
udt_send(A,sndpkt)
rdt_rcv(rcvpkt) && from_B(rcvpkt) && (corrupt(rcvpkt) || has_seq1(rcvpkt))
sndpkt=make_pkt(ACK, 1, checksum)
udt_send(B,sndpkt)
rdt_rcv(rcvpkt)&&from_A(rcvpkt)&&not_corrupt(rcvpkt)&&has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt=make_pkt(ACK,0,checksum)
udt_send(A,sndpkt)
(1)
(2)
(3)
(4)
(5)
(6)
rdt_rcv(rcvpkt)&&not_corrupt(rcvpkt)&&has_seq0(rcvpkt)&&from_B(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt=make_pkt(ACK,0,checksum)
udt_send(B,sndpkt)
Notes: Note: When receiving from the wrong host (e.g., (1), (4)), can also do nothing (i.e., Λ). If a sender x is waiting on ack for previous packet (due to lost/corrupted ack), the receiver will resend that ack later when “wait for ... from x”.

## Slide 40: Extension: one-to-multi rdt
Q: How to ensure A transmits the same data to both B and C in the presence of errors/losses? (broadcast channel, independent errors/losses)
A
B
C
A: Receiver B or C is the same as the receiver in rdt2.2!

## Slide 41: Extension: one-to-multi rdt
Sender A
Wait for call 0
from above
Wait for ACK 0
from B or C
Wait for ACK 1
from B
Wait for ACK 0
from C
Wait for ACK 0
from B
Wait for call 1
from above
Wait for ACK 1
from B or C
Wait for ACK 1
from C
(1)
(2)
(3)
(4)
(5)
(6)
(3)
(7)
(3)
(8)
(5)
(6)
(9)
(10)
(11)
(12)
(13)
(14)
(15)
(16)
(17)
(18)
(19)
(20)

## Slide 42: Extension: one-to-multi rdt
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& isACK(rcvpkt,0,B))
Λ
Sender A (cont’d)
rdt_rcv(rcvpkt)
Λ
(1)
(2)
(3)
rdt_send(data)
sndpkt=make_pkt(0,data,checksum)
udt_send(sndpkt)
start_timer
(4)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
|| isACK(rcvpkt,1,B) || isACK(rcvpkt,1,C))
Λ
timeout
udt_send(sndpkt)
start_timer
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& isACK(rcvpkt,0,C))
Λ
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
|| !isACK(rcvpkt,0,C))
Λ
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
|| !isACK(rcvpkt,0,B))
Λ
(5)
(6)
(7)
(8)

## Slide 43: Review
rdt1.0: no error
rdt2.0: error at receiver
  ACK/NAK
rdt2.1: error at sender & receiver
  ACK/NAK, sequence number (0/1)
rdt2.2: similar to rdt2.1, but only ACK
  including sequence number in ACK
rdt3.0: error & loss
  sequence#, timer
Notes: End of lecture 3

## Slide 44: Performance of rdt3.0
rdt3.0 is correct, but performance stinks
e.g.: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  sender utilization – fraction of time sender busy sending
  RTT=30 msec, 8K bits every 30 msec: 264 Kbps throughput over 1 Gbps link!
Dtrans =
L
R
8000 bits
10 9 bits/sec
=
=
8 microsecs
t = 0
t = L / R
sender
receiver
RTT
send next packet
t = RTT + L / R
Notes: assuming speed of light as propagation speed, 15 ms prop. delay -> 4500 km length. (like a transatlantic cable!)

## Slide 45: Pipelined protocols
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver

## Slide 46: Pipelined protocols: overview
Go-back-N:
sender can have up to N unacked packets in pipeline
receiver only sends cumulative ack
  doesn’t ack packet if there’s a gap
sender has timer for oldest unacked packet
  when timer expires, retransmit all unacked packets
Selective Repeat:
sender can have up to N unacked packets in pipeline
receiver sends individual ack for each packet
sender maintains timer for each unacked packet
  when timer expires, retransmit only that unacked packet
common
different

## Slide 47: Go-Back-N: sender
“window” of up to N, consecutive unack’ed pkts allowed
timer for oldest in-flight pkt
timeout(n): retransmit packet n and all higher seq # pkts in window

## Slide 48: Go-Back-N: receiver
(a) Sender view of sequence numbers
(b) Receiver view of sequence numbers
expectedseqnum
already ack’ed
acceptable
unacceptable
Window size
N
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
Notes: Expectedseqnum-N <= send_base <= expectedseqnum
If totally M distinct sequence numbers, #states for the sender = M(N+1), #states for the receiver = M.

## Slide 49: GBN: sender extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
If base <= getacknum(rcvpkt) {
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
}
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=0
nextseqnum=0
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L
L
Notes: Using FSM, we will need a separate state for each combination of (send_base, nextseqnum)! -> collapse the states, use state variables (extended FSM)

## Slide 50: GBN: receiver extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer): no receiver buffering!
  re-ACK pkt with highest in-order seq #
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=0
sndpkt =
make_pkt(-1,ACK,chksum)
L

## Slide 51: GBN in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
…

## Slide 52: Review
Performance analysis:
  Utilization of stop-and-wait protocol
  Utilization of pipelined protocol
Pipelined protocols:
  Go-Back-N
  Selective Repeat
Notes: End of lecture 4

## Slide 53: Selective repeat
sender: individually tracks timeout of inflight pkts
  maintain timer for each unACKed pkt
  only resend the pkt causing timeout
receiver: individually acknowledges each correctly received pkt
  buffers out-of-order pkts for eventual in-order delivery to application layer

## Slide 54: Selective repeat: sender, receiver windows

## Slide 55: Selective repeat
data from above:
if next seq# n is in window, send pkt(n), start timer(n)
timeout(n):
resend pkt(n), restart timer(n)
ACK(n) in [sendbase, sendbase+N]:
mark pkt(n) as received, stop timer(n)
if n is the smallest unACKed seq#, advance window base to next unACKed seq #
sender
pkt seq# n in [rcvbase, rcvbase+N-1]
send ACK(n)
if out-of-order: buffer
if in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt seq# n in [rcvbase-N, rcvbase-1]
send ACK(n)
otherwise:
ignore
receiver

## Slide 56: GBN in action (recall)
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
…
10 transmissions in total

## Slide 57: Selective repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
X
loss
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
record ack3 arrived
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
record ack4 arrived
record ack5 arrived
Q: what happens when ack2 arrives?
7 transmissions in total
Notes: A: advance send_base to the next unACKed seq#, which is 6.

## Slide 58: Selective repeat: dilemma
example:
seq #’s: 0, 1, 2, 3
window size=3
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
receiver can’t see sender side.
receiver behavior identical in both cases!
something’s (very) wrong!
receiver sees no difference in two scenarios!
duplicate data accepted as new in (b)
Notes: A: Window size <= half of sequence number size.

## Slide 59: Selective repeat: dilemma
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 4 5 0
0 1 2 3 4 5 0
0 1 2 3 4 5 0
pkt0
pkt1
pkt2
0 1 2 3 4 5 0
pkt0
timeout
retransmit pkt0
0 1 2 3 4 5 0
0 1 2 3 4 5 0
0 1 2 3 4 5 0
X
X
X
will ignore packet
with seq number 0
b) correct
Q: what relationship between size of seq # space and window size to avoid problem in (b)?
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
a) incorrect
A: window size ≤ (#sequence numbers)/2
Notes: A: Window size <= half of sequence number size.
Q: how about GBN?
A: As long as #seq numbers > N, the receiver will not deliver duplicate packets (worst case, receiver waiting for seq N, sender sends seq 0,1,...,N-1). -> minimum #seq numbers for GBN is N+1.
Note that #seq numbers = N will not work, as the receiver could wait on the next size-N window with starting seq# 0, while sender resends 0,1,...,N-1.

## Slide 60: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 61: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 62: TCP seq. numbers, ACKs
sequence numbers:
  byte stream “number” of first byte in segment’s payload
acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
sent
ACKed
sent, not ACKed
usable,
not sent
not
usable
window size
N
  A’s sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from A
ACKed
acceptable
not acceptable
  B’s sequence number space
View of A
Host B
Host A

## Slide 63: TCP seq. numbers, ACKs
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
simple telnet scenario
Host B
Host A
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
At the beginning: For Host A, everything up to byte 41 has been acked, everything up to 78 has been corrected received.
Notes: from A’s perspective: at the beginning, everything up to byte 41 has been acked, everything up to 78 has been corrected received.

## Slide 64: Review
Pipelined protocols:
  Go-Back-N
  Selective Repeat
TCP basics:
  segment structure
  bidirectional communication
  byte stream-based sequence/acknowledgement #
Notes: End of lecture 5

## Slide 65: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 66: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
  pipelined segments
  cumulative acks
  single timer
  retransmit a single pkt upon timeout
let’s initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control

## Slide 67: TCP sender (simplified)
wait
for
event
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
L
create segment, seq. #: NextSeqNum
pass segment to IP (i.e., “send”)
NextSeqNum = NextSeqNum + length(data)
if (timer currently not running)
start timer
data received from application above
retransmit not-yet-acked segment causing timeout
start timer
timeout
if (y > SendBase) {
SendBase = y
/* SendBase–1: last cumulatively ACKed byte */
if (there are currently not-yet-acked segments)
start timer
else stop timer
}
ACK received, with ACK# y
Notes: as in previous rdt senders, TCP sender needs to respond to 3 types of events: call from above, call from below, timeout.

## Slide 68: TCP receiver (simplified)
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,AckNum)
extract(rcvpkt,data)
deliver_data(data)
AckNum = AckNum + length(data)
sndpkt = make_pkt(AckNum,ACK,chksum)
udt_send(sndpkt)
AckNum=InitialAckNum
sndpkt =
make_pkt(InitialAckNum-1,ACK,chksum)
L
Could buffer out-of-order data
Notes: Modified from Go-Back-N receiver (replacing ExpectedSeqNum by AckNum)
“default”: send a duplicate ACK
successful: send a new ACK

## Slide 69: TCP: retransmission scenarios
(a) lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
timeout
ACK=100
X
(b) cumulative ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120
Notes: mark SendBase and AckNum on the time rail graph

## Slide 70: Boost: TCP fast retransmit
timeout is often long
idea: detect lost pkt via duplicate ACKs
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs.
if sender receives 3 duplicate ACKs, resend the oldest unacked segment
TCP fast retransmit
X
fast retransmit after sender
receives triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Notes: Note: after receiving the first ACK 100, SendBase is advanced (to 100), and timer is restarted.

## Slide 71: Parameter setting
timeout
  how long is “too long”?
N
  how fast to transmit?

## Slide 72: TCP round trip time, timeout
Q: how to set TCP timeout value?
just above a “normal” RTT
Q: how to estimate RTT?
SampleRTT: measured RTT
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
Notes: too long: slow response to loss
too short: premature timeout and unnecessary retransmission

## Slide 73: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponentially weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)

## Slide 74: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
estimate SampleRTT deviation from EstimatedRTT:
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
Notes: Lecture 3.
Q(4) = 3.167e-05 (the probability of premature timeout under the above setting of timeout)
Note: The interactive exercise of Jim assumes DevRTT to be updated, then EstimatedRTT, and then TimeoutInterval, after receiving each new SampleRTT. It is also correct to update EstimatedRTT, then DevRTT, and then TimeoutInterval (although the resulting DevRTT and TimeoutInterval will be difference).

## Slide 75: Review
Determination of TCP timeout
  RTT, deviation of RTT
TCP as a rdt protocol
  Sender: pipelined transmission, cumulative acknowledgement, single retransmission (timeout/3 duplicate ACKs)
  Receiver: delayed ACK for in-order packet, immediate ACK for gap/recovery
Notes: End of lecture 6

## Slide 76: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 77: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application may
remove data from
TCP socket buffers ….
… slower than TCP
receiver is delivering
(sender is sending)
from sender
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control

## Slide 78: TCP flow control
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
receiver advertises free buffer space by including rwnd value in TCP header (“receive window” field)
sender limits amount of unacked (“in-flight”) data to receiver’s rwnd value
guarantees receive buffer will not overflow
receiver-side buffer
Notes:   RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems auto-adjust RcvBuffer

## Slide 79: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 80: TCP congestion control:
approach: sender increases transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase cwnd by 1 MSS every RTT until loss detected
  multiplicative decrease: cut cwnd in half after loss
cwnd: TCP sender
congestion window size
AIMD saw tooth
curve
additively increase window size …
…. until loss occurs (then cut window in half)
time

## Slide 81: TCP Congestion Control: details
sender limits transmission:
usually cwnd < rwnd
  dynamic function of perceived network congestion
<
LastByteSent-
LastByteAcked
min(rwnd,cwnd)
last byte
ACKed
sent, not-yet ACKed
(“in-flight”)
last byte sent
cwnd
sender sequence number space

## Slide 82: Update cwnd: TCP Slow Start
when connection begins, increase cwnd as follows until first loss event or cwnd ≥ ssthresh:
  initially cwnd = 1 MSS
  incrementing cwnd by 1 MSS for every ACK received
  → double cwnd every RTT
Host A
one segment
RTT
Host B
time
two segments
four segments
MSS: maximum #bytes in the payload of a TCP segment
Notes: MTU (maximum transmission unit): maximum #bytes in the payload of a link-layer frame (usually an IP datagram)
Typically, MSS = MTU - 40 (20-byte TCP header + 20-byte IP header).

## Slide 83: Update cwnd: TCP Congestion Avoidance
when cwnd ≥ ssthresh, increase rate additively until first loss event:
  incrementing cwnd by MSS2/cwnd for every ACK received
  → Increase cwnd by 1 MSS every RTT
Host A
RTT
Host B
time
four segments
five segments

## Slide 84: TCP: detecting, reacting to loss
loss indicated by timeout:
  cwnd set to 1 MSS
  go back to slow start
loss indicated by 3 duplicate ACKs:
  TCP RENO: cwnd is cut in half
  TCP Tahoe: cwnd is set to 1 MSS
Notes: 3-duplicate ACKs: cwnd = cwnd/2 + 3 (set ssthreshold = cwnd/2).

## Slide 85: TCP: switching from slow start to CA
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before the last loss
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 86: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3MSS
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3MSS
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0

## Slide 87: TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. throughput is ¾ W per RTT
W
W/2
avg TCP thruput =
3
4
W
RTT
bytes/sec

## Slide 88: Chapter 3: summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
next:
leaving the network “edge” (application, transport layers)
into the network “core”
two network layer chapters:
  data plane
  control plane
Notes: end of lecture 7.

## Slide 89: backup slides

## Slide 90: Internet transport-layer protocols
reliable, in-order delivery: TCP
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  none of the above
services not available:
  delay guarantees
  throughput guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 91: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server

## Slide 92: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!

## Slide 93: Selective repeat vs. Go-Back-N
Go-Back-N
state variables: send_base, nextseqnum, expectedseqnum
a single timer
cumulative acknowledgement
cumulative retransmission (“go back N”)
Selective Repeat
state variables: send/rcv_base, nextseqnum, state (acked/unacked) per packet
N timers
individual acknowledgement
individual retransmission (“selective repeat”)

## Slide 94: TCP: Overview RFCs: 793,1122,1323, 2018, 2581
connection-oriented:
  handshaking (exchange of control msgs) inits sender, receiver state
flow-controlled:
  sender will not overwhelm receiver
congestion-controlled:
  sender will not overwhelm network
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
full duplex data:
  bi-directional data flow in same connection
Q: how to handle out-of-order segments?
  A: TCP spec doesn’t say, - up to implementor

## Slide 95: TCP sender events:
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unacked segment
  expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ack rcvd:
if ack acknowledges previously unacked segments
  update what is known to be ACKed
  start timer if there are still unacked segments

## Slide 96: TCP ACK generation [RFC 1122, RFC 2581]
event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
Aggregate ACKs
Fast loss detection,
Fast recovery

## Slide 97: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3MSS
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3MSS
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0

## Slide 98: TCP Fairness
TCP is fair: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 99: Why is TCP fair?
two competing sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
Notes: End of lecture 7

## Slide 100: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 101: Connection Management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();

## Slide 102: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)

## Slide 103: Agreeing to establish a connection
2-way handshake failure scenarios:
retransmit
req_conn(x)
ESTAB
req_conn(x)
half open connection!
(no client!)
client terminates
server
forgets x
connection
x completes
retransmit
req_conn(x)
ESTAB
req_conn(x)
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x

## Slide 104: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN

## Slide 105: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled

## Slide 106: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB
Notes: Lecture 4.