## Slide 1: Physical Layer: “Computer Networks”, Tanenbaum, Chap2 (2.1, 2.2, 2.3, 2.5)
Functions
Fundamentals/Channel Capacity
Analog Overview
Digital Overview
Modulation
Media Types
  twisted pair
  coaxial cable
  fiber
  wireless

## Slide 2: Physical Layer
Physical Layer
  electrical/optical transmission of bits or symbols
  physical control signals
sender
receiver
packet switches
message
segment
datagram
frame
bits
Application layer
Transport layer
Network layer
Link layer
Physical layer
Application layer
Transport layer
Network layer
Link layer
Physical layer
Notes: Upper layers (2-5): all about “encapsulation”
Physical layer: all about “conversion”

## Slide 3: Periodic Signals
Peak Amplitude (A)
  maximum strength of signal
  volts
Frequency (f)
  Rate of change of signal
  Hertz (Hz) or cycles per second
  Period = time for one repetition (T)
  T = 1/f
Phase ()
  Relative position in time
Notes: Phase: represented as angle in the radial coordinate system (between 0 and 2\pi).

## Slide 4: Fourier Analysis
Fourier theorem: A periodic signal (of period T) is made up of (possibly infinite) component signals
  component signals are sine waves
  f=1/T: fundamental frequency
The component waves satisfy:
Jean-Baptiste Fourier
1768-1830
dt
dt
Notes: Fourier: a French mathematician in 18th centrury.

## Slide 5: Fourier Analysis
Fourier theorem: A periodic signal (of period T) is made up of (possibly infinite) component signals
Define: x(t):=1, yn(t):=sin(2πnft), zn(t):=cos(2πnft)
{x(t), yn(t), zn(t)} is an orthogonal basis of {periodic signals of period T}
  Fourier theorem  a basis
  Pairwise orthogonal:
dt
dt
“inner product”:
x(t) yn(t), zn(t)
yk(t) yn(t),
yk(t) zn(t)
Notes: missing “dt” in bottom two equations

## Slide 6: Fourier Analysis
A periodic signal (of period T) is made up of (possibly infinite) component signals
  component signals are sine waves
  f=1/T: fundamental frequency
The coefficients are given by:
Fourier coefficients ↔ original signal
Notes: c, a_n, b_n: strength of the signal at frequency 0, nf

## Slide 7: Why Fourier Analysis?
Transmission medium will “selectively” pass signals from 0-frequency to some cutoff frequency fc (physical property of the medium)
  no sharp cutoff  fc: frequency when power is attenuated by half (aka “bandwidth”)
ASCII code for ‘b’, represented by a discrete signal
equally attenuated at all frequencies
strongly attenuated at frequencies > fc
0.5
Notes: lecture 1.
The point in representing the signal in frequency domain is the physical medium does “frequency-selective attenuation”.
In contrast to using bandwidth to denote link capacity (bps), “bandwidth” here means how wide a frequency band can pass through the link (without being attenuated by more than half).

## Slide 8: Bandwidth-Limited Signals

## Slide 9: Bandwidth-Limited Signals
(d) – (e) Successive approximations to the original signal.

## Slide 10: Relation between Data Rate and #Harmonics
0
Notes: quality of sending ASCII characters (e.g., for web) over a regular telephone line (as in DSL network)

## Slide 11: Relation between Data Rate and #Harmonics
higher bit rate  fewer harmonics  higher bit error rate
Computer Networks, Fifth Edition by Andrew Tanenbaum and David Wetherall, © Pearson Education-Prentice Hall, 2011

## Slide 12: Review
Physical layer service
Signal composition:
  Fourier analysis
Notes: End of lecture 1.

## Slide 13: Analog and Digital Data Transmission
Data
  Logical entities that convey meaning (e.g., content of a call, content of a file)
  can be continuous (analog data) or discrete (digital data)
Signals
  Physical representations of data (e.g., electric pulse, electromagnetic wave)
  Signal is the means by which data are propagated
  can be continuous (analog signal) or discrete (digital signal)
Can use analog signal to carry digital data
  Modem
Can use digital signal to carry analog data
  Compact Disc audio
Notes: Can have all 4 combinations:
Digital Data, Analog Signal
Analog Data, Digital Signal
Analog Data, Analog Signal
Digital Data, Digital Signal

## Slide 14: Modulation and Coding
Digital Data, Analog Signal
Analog Data, Digital Signal
Analog Data, Analog Signal
Digital Data, Digital Signal
Notes: Modulation: modify a base signal to encode information in the data

## Slide 15: Digital Data Modulation
Modem
  modulator (D-to-A converter) & demodulator (A-to-D converter)
Two classes of modulation schemes:
baseband modulation
  signal occupies frequency from 0 to a cutoff frequency
  common for wired channels
passband modulation
  signal occupies a shifted frequency band (not starting from 0)
  common for wireless channels
0
fc
frequency
0
frequency
Notes: Example for passband “carrier frequency”: 0.9-6 GHz
Millimeter wave: frequency 30-300 GHz

## Slide 16: Baseband Modulation
Common for wired channels
Basically aim at encoding a sequence of 0’s and 1’s by two voltage levels
Schemes (aka line codes):
  Nonreturn to Zero (NRZ)
  Nonreturn to Zero Inverted (NRZI)
  Biphase: Manchester, Differential Manchester
  Bipolar: Alternate Mark Inversion (AMI)
Pay attention to 2 properties: whether the code is (1) self-synchronized, (2) balanced
“self-synchronized signal”: allows receiver to detect boundaries of bit intervals
“balanced signal”: positive voltages and negative voltages average to ~zero
  non-zero average  DC component  wasted energy (DC component will be filtered out)
  balanced signal can be used to calibrate receiver: use the average as detection threshold
Notes: Basically about how to represent 0/1 by two different voltage levels
“balanced signal”: having equal portions of positive and negative voltage (average to zero) -> balanced signal is good because there is no DC component, which will be filtered out (strongly attenuated by some media or receiver) and hence waste energy.

## Slide 17: Nonreturn to Zero (NRZ)
Two different voltages for 0 and 1 bits
E.g. negative voltage for 0, positive voltage for 1
Voltage constant during bit interval
  no transition, i.e., “no return to zero voltage”
Intuitive, but seldom used in practice

## Slide 18: Nonreturn to Zero Inverted (NRZI)
NRZ causes synchronization issues when sending long runs of 0’s or 1’s
  the signal looks almost identical when sending a run of 100 0’s and a run of 101 0’s
Idea: Data encoded as presence or absence of signal transition
  Transition (low-to-high or high-to-low) denotes a 1
  No transition denotes a 0
An example of “differential encoding”, used in USB (Universal Serial Bus)
Q: How about long runs of 0’s?
A: code the bit sequence to “break up” the 0’s (see Figure 2-21. 4B/5B mapping)
Notes: A: code a group of bits to a slightly longer group of bits that does not contain long runs of 0’s, e.g., 4B/5B code (see textbook Figure 2-21)

## Slide 19: Biphase
Idea: Send both the data and the clock signal
Manchester
  Transition in middle of each bit period, transmitted signal = clock XOR data
  Low to high represents 0
  High to low represents 1
  Used by IEEE 802.3 (Ethernet)
Differential Manchester
  End-of-bit transition is only clocking
  Mid-bit transition represents 0
  No mid-bit transition represents 1
  Note: this is also a differential encoding scheme
  Used by IEEE 802.5 (token ring)
data
signal

## Slide 20: Bipolar Encoding (Alternate Mark Inversion (AMI))
Biphase codes (Manchester & differential Manchester) are balanced
Another balanced code: Alternate Mark Inversion (AMI)
  3 voltage levels: -1 V, 0 V, +1 V
  zero is represented by 0 V
  one is represented by +1 or -1 V alternatingly
Notes: Besides clock synchronization, another desirable property of signal is “balancing”.
Bipolar code (AMI) is more energy efficient.

## Slide 21: Summary of Line Codes (for Baseband Transmission)
Computer Networks, Fifth Edition by Andrew Tanenbaum and David Wetherall, © Pearson Education-Prentice Hall, 2011
line code | synchronized | balanced
NRZ | N | N
NRZI | Y* | N
Biphase | Y | Y
Bipolar | N | Y

## Slide 22: Review
Digital data  signal conversion
  modulation for baseband transmission
  modulation for passband transmission
Notes: End of lecture 2.

## Slide 23: Passband Modulation
  Common for wireless channels
Signal occupies a shifted frequency band (not starting from 0)
    data encoded by modifying (“modulating”) a carrier signal
0
frequency
carrier signal

## Slide 24: Methods for Passband Modulation
(a) A binary signal
(b) Amplitude modulation
(c) Frequency modulation
(d) Phase modulation
Notes: The idea of passband modulation is to start with a baseline signal within the targeted frequency band, e.g., a sine wave with that frequency, and modify one or multiple parameters of the baseline signal to encode information.

## Slide 25: Amplitude Shift Keying
Values represented by different amplitudes of carrier
Usually, one amplitude is zero
  i.e. presence and absence of carrier is used
Susceptible to sudden gain changes
Inefficient
Used over optical fiber
Notes: * Shift Keying is a physical layer jargon for saying “*-based modulation”

## Slide 26: Frequency Shift Keying
Values represented by different frequencies (near carrier)
Less susceptible to error than ASK
High frequency radio
Even higher frequency on LANs using co-ax

## Slide 27: Phase Shift Keying
Phase of carrier signal is shifted to represent data
Binary Phase Shift Keying (BPSK):
Quadrature Phase Shift Keying (QPSK): More efficient use of channel by letting each signal element representing more than one bit
  e.g. shifts of {0, /2, , 3/2} or {/4, 3/4, 5/4, 7/4}
  Each element represents two bits
  Can use 8 phase angles and have more than one amplitude
  9600bps modem use 12 angles, four of which have two amplitudes
Notes: skipped material:
Differential PSK
  Phase shifted relative to previous transmission rather than some reference signal

## Slide 28: Quadrature Amplitude Modulation
Simultaneously modulate phase and amplitude to transmit data at a higher rate
For example:
Quadrature Phase Shift Keying (QPSK): Use 4 shift values to represent two bits per signal element
  e.g. shifts of {0, /2, , 3/2} or {/4, 3/4, 5/4, 7/4}
  Each element represents 2 bits (i.e., log2 4)
Quadrature Amplitude Modulation (QAM)-16: Use 12 phase shifts, 4 of which have 2 amplitude levels
  #possible signal elements = 8 + 4*2 = 16
  Each element represents 4 bits (i.e., log2 16)

## Slide 29: Constellation diagram
(a) QPSK.
(b) QAM-16.
(c) QAM-64.
An easier way of representing possible signal elements (symbols) of a modulation scheme
phase
amplitude
2 bits/symbol
4 bits/symbol
6 bits/symbol

## Slide 30: Decoding example: QAM
Computer Networks, Fifth Edition by Andrew Tanenbaum and David Wetherall, © Pearson Education-Prentice Hall, 2011
Gray-coded QAM-16
Tradeoff: higher data rate  higher error rate

## Slide 31: Review
Digital data  signal conversion
  baseband: line codes
  passband: ASK, FSK, PSK, QAM
Notes: End of lecture 3.

## Slide 32: Transmission Media
Guided
  Twisted Pair
  Coaxial cable
  Optical fiber
Free space (unguided)
  Wireless
Notes: signal impairments: attenuation, noise, multipath fading, interference

## Slide 33: Transmission Media
Guided
  Twisted Pair
    telephone network, DSL, Ethernet
    amplifiers every 5km to 6km
    repeater every 2km or 3km
  Coaxial cable
    TV network, Cable
    amplifiers every few km
    repeater every 1km
  Optical fiber
    backbone, datacenter, HPC
    repeater spaced 10s of km
Free space
  Wireless
    single hop
    multi-hop allowed
T
T + t
or
transmitter
transmitted signal
receiver
received signal
other transmitter
Notes: signal impairments: attenuation, noise, multipath fading, interference

## Slide 34: Summary of Physical Layer
Physical layer fundamentals
  Fourier analysis, signal vs. data, analog vs. digital, data rate vs. bandwidth
Modulation
  digital  analog, analog  digital, analog  analog, digital  digital
Media Types
  guided: twisted pair, coaxial cable, fiber
  free-space: wireless
Notes: End of lecture 4.

## Slide 35: Synthesis: a day in the life of a web request
Journey down protocol stack complete!
  application, transport, network, link, physical
Putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in a seemingly simple scenario: requesting a web page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 36: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 37: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet, modulated by Manchester code
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 38: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of local DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded through LAN, demultiplexing at client
Client now has IP address, knows name & addr of local DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 39: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 40: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 41: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established (for client!)
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 42: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
Notes: Lecture 4.

## Slide 43: Skipped slides

## Slide 44: Transmission Impairments
Signal received may differ from signal transmitted
Analog - degradation of signal quality
Digital - bit errors
Caused by
  Attenuation
  Delay distortion
  Noise
  Interference
Q: How to reduce impairments?
A: Strategy differs for analog/digital transmission
Notes: So how do we fight these impairments? The strategy differs based on the type of signal transmitted.

## Slide 45: Analog Transmission
Analog signal transmitted without regard to content
  May be analog or digital data
Attenuated over distance
Use amplifiers to boost signal
  Also amplifies noise!
Amplify-and-forward

## Slide 46: Digital Transmission
Intermediate nodes aware of content
Integrity endangered by noise, attenuation etc.
Repeaters used, which
  receives signal
  Extracts bit pattern
  Retransmits
Overcome signal attenuation without amplifying noise!
Advantages over analog transmission:
  data integrity: lower error rate, longer distance
decode-and-forward

## Slide 47: Modulation and Coding
Digital Data, Analog Signal
Analog Data, Digital Signal
Analog Data, Analog Signal
Digital Data, Digital Signal

## Slide 48: Analog Data, Digital Signal
Digitization
  Conversion of analog data into digital data
  Digital data can then be transmitted
    The transmission may first convert the digital data back to an analog signal (different from original)
  The conversion done using a codec
Notes: Actually 2-step process: analog data -> digital data -> digital/analog signal

## Slide 49: Pulse Code Modulation (PCM)
Nyquist Sampling Theorem: If a signal is sampled at regular intervals at a rate higher than twice the highest signal frequency, the samples contain all the information of the original signal.
Example: Voice data limited to below 4000Hz
  Require 8000 sample per second
  Each sample assigned digital value  Quantization
  E.g., 4-bit quantization gives 16 levels, 8-bit quantization gives 256 levels
  To modulate voice with 256 levels, we need 8000 samples/sec of 8 bits each  data rate is 64 kbps
 Tradeoff: more bits per sample means smaller quantization error but more bits generated
8 9 11 13 14 15 15 15 ...
10001001101111011110111111111111 ...

## Slide 50: Review
Digital data  analog signal conversion
  baseband: line codes
  passband: ASK, FSK, PSK, QAM
Analog data  digital signal conversion
  sampling, quantization
Notes: End of lecture 3.

## Slide 51: Analog Signals Carrying Analog and Digital Data

## Slide 52: Digital Signals Carrying Analog and Digital Data
Data
Notes: this is about recording audio on CD

## Slide 53: Channel Capacity
Data rate
  In bits per second
  Rate at which data can be communicated
Bandwidth
  In cycles per second or Hertz
  Constrained by transmitter and medium
The two are proportional to each other:
Nyquist Theorem (noiseless channel): maximum data rate = 2B log2V bits/sec
  B – channel bandwidth (must sample at twice this rate)
  V – discrete levels of signal (e.g., 2 if we are using 1 and 0)
Shannon’s Theorem (noisy channel): maximum data rate = 2B log2(1 + S/N) bits/sec
  B – channel bandwidth
  S – signal power
  N – noise power

## Slide 54: Modulation Rate

## Slide 55: Delta Modulation
Analog input is approximated by a staircase function
Move up or down one level () at each sample interval
Binary output: 1 - moving up, 0 - moving down
easier to compress

## Slide 56: Modulation and Coding
Digital Data, Analog Signal
Analog Data, Digital Signal
Analog Data, Analog Signal
Digital Data, Digital Signal

## Slide 57: Analog Data, Analog Signals
Why modulate analog signals?
  Higher frequency can give more efficient transmission
  Permits frequency division multiplexing (chapter 8)
Types of modulation
  Amplitude
  Frequency
  Phase

## Slide 58: Analog Modulation

## Slide 59: Modulation and Coding
Digital Data, Analog Signal
Analog Data, Digital Signal
Analog Data, Analog Signal
Digital Data, Digital Signal

## Slide 60: Digital Data, Digital Signal
Digital signal
  Discrete, discontinuous voltage pulses
  Each pulse is a signal element
  Binary data encoded into signal elements

## Slide 61: Transmission Media
Guided
  Twisted Pair
  Coaxial cable
  Optical fiber
Free space
  Wireless

## Slide 62: Twisted Pairs
Category 5 UTP cable with four twisted pairs
Computer Networks, Fifth Edition by Andrew Tanenbaum and David Wetherall, © Pearson Education-Prentice Hall, 2011

## Slide 63: Twisted Pair
Most common medium
Telephone network
  Between house and local exchange (subscriber loop)
Within buildings
  To private branch exchange (PBX)
For local area networks (LAN)
  10Mbps or 100Mbps
Analog
  Amplifiers every 5km to 6km
Digital
  Use either analog or digital signals
  repeater every 2km or 3km
Limited distance
Limited bandwidth (1MHz)
Limited data rate (100MHz)
Susceptible to interference and noise

## Slide 64: Coaxial Cable
Most versatile medium
Television distribution
  Ariel to TV
  Cable TV
Long distance telephone transmission
  Can carry 10,000 voice calls simultaneously
  Being replaced by fiber optic
Short distance computer systems links
Local area networks
Analog
  Amplifiers every few km
  Closer if higher frequency
  Up to 500MHz
Digital
  Repeater every 1km
  Closer for higher data rates

## Slide 65: Fiber Cables
Greater capacity
  Data rates of hundreds of Gbps
Smaller size & weight
Lower attenuation
Electromagnetic isolation
Greater repeater spacing
  10s of km at least
Long-haul trunks
Metropolitan trunks
Rural exchange trunks
Subscriber loops
LANs

## Slide 66: Fiber Optics (1)
Three examples of a light ray from inside a silica fiber impinging on the air/silica boundary at different angles.
Computer Networks, Fifth Edition by Andrew Tanenbaum and David Wetherall, © Pearson Education-Prentice Hall, 2011

## Slide 67: Fiber Optics (2)
Light trapped by total internal reflection.
Computer Networks, Fifth Edition by Andrew Tanenbaum and David Wetherall, © Pearson Education-Prentice Hall, 2011

## Slide 68: Transmission of Light Through Fiber
Attenuation of light through fiber in the infrared region
Computer Networks, Fifth Edition by Andrew Tanenbaum and David Wetherall, © Pearson Education-Prentice Hall, 2011

## Slide 69: Wireless Transmission
Multipath fading
Rayleigh Fading
  statistical model of fading over the air
Distortion
  can be combated with equalizers
Shadows
  obstructions
T
T + t
or

## Slide 70: Channels
Allow more than one session to take place on a single physical link
Increases network capacity

## Slide 71: Frequency Division Multiplexing
(a) The original bandwidths.
(b) The bandwidths raised in frequency.
(b) The multiplexed channel.

## Slide 72: Wireless Access Basics
Frequency Division Multiple Access (FDMA):
e.g. the analog cellular system: 1G
Time Division Multiple Access (TDMA):
e.g. IS-54 and IS-136, GSM, PDC: 2G
GPRS: 2.5G
UWC-136, EDGE: 3G
Code Division Multiple Access (CDMA):
e.g. IS-95A,B (cdmaOne) : 2G
IS-2000 (cdma2000), WCDMA : 3G
4

## Slide 73: Wavelength Division Multiplexing
Wavelength division multiplexing.

## Slide 74: Time Division Multiplexing
Time Division Multiplexing (TDM).
Computer Networks, Fifth Edition by Andrew Tanenbaum and David Wetherall, © Pearson Education-Prentice Hall, 2011

## Slide 75: Time Division Multiplexing
The T1 carrier (1.544 Mbps).

## Slide 76: Time Division Multiplexing (3)
Multiplexing T1 streams into higher carriers.